linux sound synthesizer

by Malte Steiner, block 4

Minicomputer is an open source sound synthesizer for Linux, distributed under the GPL 3 license. It requires jack as an audioserver and Alsa for midi connection. Minicomputer is a standalone application, divided into two programs, the actual sound engine and the editor. Both independent programs communicate via OSC (open sound control) and it is possible to write different editors or control the engine from other applications which can talk OSC.

hookup diagram

Well its software but under Linux with Alsa and Jack its rather similar to studio environments so a diagram makes sense. The editor talks to the sound core via Open Sound Control (OSC) protocol over localhost network. These both applications don't need to be connected manually and the order of launching doesn't matter, they should find each other. They communicate over the port 7770 which can be changed during compilation time in the common.h file. Normally they reside on the same machine but it could be possible, with minour changes in the source code, that they run on separate computers, connected via network.
Both provide a midi port. The editor accept Midi program changes on channel 1 – 8 for switching between the first 128 (0 – 127, a limitation of Midi specification) of the 512 sound settings. This limitation is not that bad, because on channel 9 you can switch between the 128 possible multi setups so all 8 voices can be changed at once, for instance at the beginning of a new song.

(local)network OSC
gui editor
synth engine

audio to JACK

Midi for program change

Midi for playing

The synth engine recieves note and performance data through it Midi port, channel 1 – 8 for the individual voices. It provides several audio ports for JACK for the output of sound.

There is a stereo mixed output for mixing voices together, aux 1 and aux 2 as a separete two channel output, for instance for effects, and individual outputs for each voice.

audio ports as seen on QJackctrl

Each voice has a knob for individual, aux 1, aux 2 and mix output volume, the mix is augmented with a dedicated panoramaslider while the auxilary panning need to be done with the two volume knobs if desired. Otherwise they ment to be separate outputs but its up to the user what to do with it.
the volume section on the gui editor

The volume settings are stored in the multisettings, not in the sound data.

the sound

Minicomputer doesn't ape any existing synthesizer but has a rather traditional, subtractive approach and thus is easy to operate. Its made of 8 parallel voices forming a multitemperal setup, suited for example as a drumsynth. Each voice is monophonic in itself so it can play only one key per time, additional triggers might cut off a sound of the same voice which was already on or fading.

The synthesis based on the idea to create first a rather complex wave form via two oscillators which then got shaped with an complex morphing filter which is actually made of three filters. A lowpass filter (for not losing ground) is parallel to two bandpass filters which shapes further formants. The oscillators are not bandlimited which might lead to aliasing but give on the other hand a rich tone which is important for the FM and amplitude modulation which can be happen in both directions, even in the same time. The second one has slightly different features: it can be hard synced to the first one and the second amplitude modulator only modulates the FM output
Additionally there are more modulation options like one modulation oscillator, which can go much into audio range, the only difference that its not controlled by keyboard or pitch bending. Six envelopes of the traditional ADSR format are there for a lot of parameter changing, they can be even turn into additional oscillators with the repeat button and reach also in the audio frequency range when speed up.

A fixed seventh envelope generator forms the amplitude of the output and is not available on other modulation destinations.

The sound choice of the eight mono voices can be stored into the multisetup which is handled seperatly.
Minicomputer stores the sounds in a file called miniComputer.txt which can be opend in a texteditor. Same goes for the multis which are stored in miniMulti.txt. When the editor stores something to disk it writes it first to temporary files ending with .temp, then make a backup of the former files to .bak and then finally commit the changes be renaming the temp files to the actual names. This is done for your convenience and savety and you shouldnt have files with same names like mentioned above in the minicomputer directory, otherwise they got overwritten.

The editor got a reduced minimal design which I actually like and bear in mind that a software doesn't sound better if you slap a photo or rendering of an actual device on it. We are in the virtual domain so what.
The same goes with the sound which is simular but different to the precursor synth Microcomputer which I offerd as a shareware VSTi Plugin on Windows and Mac OS 9 some years ago. It can sound very analogue but also very digital and I didnt had any actual hardware synthesizer in mind to copy.